## Slide 1
CR/SR A1A
Pedestrian Safety & Mobility Study
RIVER TO SEA
TRANSPORTATION PLANNING ORGANIZATION
Technical Coordinating Committee/Citizens Advisory Committee Meeting | October 20, 2015

## Slide 2
PROJECT OVERVIEW + SCHEDULE

## Slide 3
Project Overview
Primary Goal
Recommend implementable pedestrian/bicycle safety improvements/countermeasures at strategic locations along A1A
Secondary Goal
Expand countermeasures to be applicable along other sections of A1A in a systemic manner
Study Limits
Bethune Beach (Volusia County) to just south of Marineland (Flagler County) – 56.5 total miles in length

## Slide 4
Project Schedule
Previous Studies Research & Crash Data Analysis | August – September
Stakeholder Meeting | Today
Focus Areas Crash Analysis/Field Reviews | October – December
Stakeholder Involvement
Systemic Countermeasure Identification | December – January
Steering Committee Workshop | January
Prioritize Systemic Countermeasures | February
Draft Report | February – March
R2CTPO + Stakeholder Review
Final Report | April
Notes: Previous Studies Research & Crash Data Analysis | August – September
Stakeholder Meeting | Today
Focus Areas Crash Analysis/Field Reviews | October – December
Stakeholder Involvement
Systemic Countermeasure Identification | December – January
Steering Committee Workshop | January
Prioritize Systemic Countermeasures | February
Draft Report | February – March
R2CTPO + Stakeholder Review
Final Report | April

## Slide 5
SUMMARY OF PREVIOUS STUDIES

## Slide 6
Previous Studies Review
Four studies performed along A1A between 2008 and 2015:
  SR A1A Pedestrian Safety Study, Daytona Beach Shores (2015)
    Recommendations included adding new mid-block crosswalks, adding Rectangular Rapid Flashing Beacons (RRFBs), and modifying markings/signs at existing crossings
  Pedestrian Safety Audit Report, Daytona Beach (2014)
    FDOT performed a pedestrian road safety audit from Earl Street to Oakridge Boulevard, proposing short, near, and long-term countermeasures along corridor
  Pedestrian Safety Study for CR A1A, New Smyrna Beach (2012)
    Recommendations included installing continuous bike facilities, sidewalks where missing, RRFBs, median refuge islands, among others
  CR A1A Sidewalk Feasibility Study, Daytona Beach Shores (2008)
    Recommendations included road diet, constructing 8’ sidewalk, consolidating driveways, and installing crosswalks

## Slide 7
LAW ENFORCEMENT COORDINATION

## Slide 8
Law Enforcement Coordination
Uniform Traffic Citation (UTC)
  UTC data does not have location information that lends itself to mapping
  Sorted through data by jurisdiction, narrowed non-crash citations to relevant hazardous moving violations
  Pedestrian and bicycle citations accounted for 1.1% of overall citation data (role of warnings)
  Pedestrian/bicycle citation detail revealed specific subsections and violations

## Slide 9
Law Enforcement Coordination
Face-to-face meetings or phone calls with Police Chiefs and traffic supervisors of law enforcement agencies along A1A
  High degree of interest in the project
  Consensus that this is a high priority traffic safety issue
  Nature of the problem differs among jurisdictions (road users, roadway conditions, pedestrian features)
  Enthusiasm for future participation in project and FDOT HVE funding

## Slide 10
CRASH DATA + FOCUS AREAS

## Slide 11
Crash Data Collection
Six years of pedestrian/bicycle crash data collected 2009 – 2014
95 pedestrian and 63 bicycle totaling 158 crashes
  14 fatal, 128 injury, and 16 property damage only
  39% occurred at night, 14% alcohol and/or drug related
  20% occurred with a pedestrian/bicyclist under the age of 20 and 18% occurred with 65 and older
Notes: Under 20 was highest of all age groups.

## Slide 12
Crash Data Analysis
Reviewed each segment for total crash frequency and crash severity weighted by crash costs
Grouped nearby 1 mile segments together to identify focus areas
Sliding Window Analysis
1 mile
0.25 mi.
1 mile
3 crashes
4 crashes
Notes: Mapped all crashes and reviewed each 1 mile segment of A1A, 0.25 miles at a time
  Ex: MP 0.00 to MP 1.00, then 0.25 to 1.25, etc.
  228 individual 1 mile segments analyzed
($10.1M for fatal, $275,400 for injury, and $7,600 for property damage)
  Analyzed top 32 one mile segments – segments with >9 crashes
  Analyzed top 55 one mile segments – segments with 1 or more fatal crashes, or in top 5 for crash frequency

## Slide 13
Crash Data Analysis
Reviewed roadway and land use metrics that potentially factor into pedestrian/bicycle crashes:
  50% of crashes on segments between 15,000 and 20,000 AADT (11.4 miles/20% of corridor length)
  62% of crashes with 30 or 35 mph posted speed
  67% of crashes on 4 lane divided (6 miles/11% corridor length) or 5 lane with two-way left-turn lane (10.6 miles/19% corridor length)
  32% of crashes away from marked crossings (both with and without active control device)
  39% of crashes under dusk, dark without street light, or dark with street light conditions
  Reviewed crashes relative to ped/bike facilities, bus stops, beach parking, parks, and civic land uses
Risked Based Analysis
Notes: In relation to Figure 9, some of the lighting was not on in Flagler Beach during the field review. Possibly due to turtle restrictions.

## Slide 14
Focus Areas Overview
Bring in Figure 10
Notes: We are choosing 3 to perform field reviews on.
Notice that south of Area A and south of SR 421 we are not proposing any focus areas because of the low crash frequency, number of pedestrian crossings currently in place

## Slide 15
Potential Field Review Locations
Recommend focus areas D, E, and G for field review
  D – Daytona Beach/Ormond Beach: 16 crashes, 4 ln divided/5 ln section
  E – Ormond Beach/Ormond-by-the-Sea: 10 crashes (3 fatal), 2 ln undivided/3 ln section
  G – Flagler Beach: 9 crashes (1 fatal), 2 ln undivided section
Could also look into reviewing focus areas A and C
  A – New Smyrna Beach: 9 crashes, 4 ln divided/5 ln section
  C – Daytona Beach: 37 crashes (2 fatal), 9 total crashes, 4 ln divided/5 ln section
    Segment from Earl St. to Oakridge Blvd. previously studied, 11 crashes from study included in data set

## Slide 16
NEXT STEPS

## Slide 17
Next Steps
Project briefing presentations to TPO Board next week
Field reviews for three focus areas – October through December
Notes:   Local law enforcement participate in field reviews
  Preparation work includes:
    Corridor specific data collection
    Crash analysis (historical, school related, pedestrian/bicycle facility)
    Crash diagram generation

## Slide 18
PROJECT CONTACT INFORMATION
R2C TPO PROJECT MANAGER:
Stephan C. Harris
Bicycle & Pedestrian Coordinator
2570 W. International Speedway Blvd.
Suite 100
Daytona Beach, FL 32114
Phone: 386.226.0422; Ext. 20428
sharris@r2ctpo.org
CONSULTANT PROJECT MANAGER:
Adam M. Burghdoff, P.E.
225 E. Robinson St.
Suite 450
Orlando, FL 32801
Phone: 386.226.0422; Ext. 20428
aburghdoff@kittelson.com