## Slide 1
Pedestrian & Bicyclist Crash Analysis 2012-2013

## Slide 2
Chart: 
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013

Bike Injury | 430 | 472 | 455 | 453 | 475 | 576 | 683



Ped Injury | 650 | 652 | 627 | 632 | 610 | 649 | 722


Pedestrian & Bicyclist
Injury Trends
Percent Change from
2007-2008 to
2012-2013

## Slide 3
Chart: Bicyclist Lighting Conditions -- Fatal Crashes
| Dark, No Street Lights | Dark, Street Lights | Daylight | Unknown
Total | 6 | 8 | 8 | 1
Chart: Bicyclist Lighting Conditions – All
| Dark, No Street Lights | Dark, Street Lights | Dawn/Dusk | Daylight | Unknown
Total | 83 | 175 | 84 | 1084 | 5
Environmental Factors

## Slide 4
Chart: Pedestrian Lighting Conditions -- Fatal
| Daylight | Dark - Lighted | Dark - Not Lighted | Dawn/Dusk
 | 18 | 36 | 39 | 4
Chart: Pedestrian Lighting Conditions -- All
| Daylight | Dark - Lighted | Dark - Not Lighted | Dawn/Dusk | other/unknown
 | 844 | 372 | 190 | 99 | 7
Environmental Factors

## Slide 5: Time & Day: Bicyclists
Chart: 
| 5 AM | 6 AM | 7 AM | 8 AM | 9 AM | 10 AM | 11 AM | 12 PM | 1 PM | 2 PM | 3 PM | 4 PM | 5 PM | 6 PM | 7 PM | 8 PM | 9 PM | 10 PM | 11 PM | 12 AM | 1 AM | 2 AM | 3 AM | 4 AM
Total | 10 | 32 | 69 | 94 | 66 | 64 | 70 | 87 | 83 | 96 | 112 | 116 | 138 | 111 | 84 | 55 | 33 | 29 | 15 | 15 | 9 | 6 | 6 | 9
Time of Day
Chart: 
| MONDAY | TUESDAY | WEDNESDAY | THURSDAY | FRIDAY | SATURDAY | SUNDAY
Total | 232 | 215 | 246 | 232 | 199 | 167 | 118
Day of Week

## Slide 6: Time & Day: Pedestrians
Chart: 
| MONDAY | TUESDAY | WEDNESDAY | THURSDAY | FRIDAY | SATURDAY | SUNDAY
Total | 220 | 231 | 211 | 221 | 261 | 202 | 169
Chart: 
| 5 | 6 AM | 7 | 8 | 9 AM | 10 | 11 | 12 PM | 1 PM | 2 PM | 3 PM | 4 PM | 5 PM | 6 PM | 7 PM | 8 PM | 9 PM | 10 PM | 11 PM | 12 AM | 1 | 2 | 3 AM | 4
Total | 22 | 54 | 51 | 65 | 55 | 70 | 53 | 73 | 77 | 74 | 103 | 92 | 90 | 111 | 104 | 89 | 87 | 61 | 35 | 45 | 34 | 40 | 11 | 19
Time of Day
Day of Week

## Slide 7
Chart: Bicyclists
Age
The number of crashes for cyclists age 16 to 21 increased 100% from 2003/04 to 2012/13, while all ages increased 42%.
Chart: Pedestrians
The number of crashes for pedestrians age 16 to 21 increased 40% from 2003/04 to 2012/13, while all ages increased 8%.

## Slide 8
Chart: Bicyclist Position Prior to Crash
| Sidewalk / Crosswalk/ Driveway Crossing | Travel lane | Bike Lane / Paved Shoulder | Non-Roadway | Multi-use Path | Other / Unknown
 | 889 | 230 | 140 | 84 | 18 | 70
Location Characteristics
Chart: Number of Lanes
| 6+ | 4 | 2 | NA
Number of Lanes | 0.26606 | 0.37919 | 0.30587 | 0.048184
# | 381 | 543 | 438 | 69

## Slide 9
Chart: Pedestrian Crash Location
| Intersection | Intersection-Related | Non-Intersection | Non-Roadway | Unknown
Total | 456 | 36 | 655 | 375 | 3
Location Characteristics
Chart: Number of Lanes
| 6 or More Lanes | 4 Lanes | 2 Lanes | NA
Number of Lanes | 0.2118 | 0.28197 | 0.2977 | 0.20852
Column1 | 323 | 430 | 454 | 318

## Slide 10
Bicyclist Crash Behaviors
Chart: Bicyclist Direction of Travel
| Facing Traffic | With Traffic | Not Applicable (Crossing) | Unknown
Percent | 0.50419 | 0.37011 | 0.087989 | 0.037011
Number | 722 | 530 | 126 | 53

## Slide 11
Crash Type | Bicyclist at Fault | Motorist at Fault | Fault Unknown | Total
Bicyclist Failed to Yield | 12 |  |  | 12
Bicyclist Right Turn / Merge | 2 |  |  | 2
Motorist Overtaking Bicyclist | 1 | 3 |  | 4
Motorist Loss of Control / Turning Error |  | 3 |  | 3
Motorist Left Turn / Merge |  | 1 |  | 1
Motorist Right Turn / Merge |  |  | 1 | 1
Grand Total | 15 | 7 | 1 | 23
Bicyclist Crash Behaviors
Behaviors for Fatal Bicyclist Crashes

## Slide 12
Crash Type | Motorist at Fault | Pedestrian at Fault | Both at Fault | Neither at Fault | Cannot Determine Fault | Total
Pedestrian Failed to Yield |  | 44 |  |  |  | 44
Non-intersection - Other/Unknown |  | 6 | 1 |  | 2 | 9
Walking Along Roadway With Traffic – Hit From Behind |  | 3 | 2 |  |  | 5
Dash |  | 5 |  |  |  | 5
Disabled Vehicle-Related | 2 | 3 |  |  |  | 5
Motor Vehicle Loss of Control | 5 |  |  |  |  | 5
Motorist Failed to Yield | 3 |  |  |  |  | 3
All Other | 2 | 9 | 2 | 2 | 6 | 21
Total | 12 | 70 | 5 | 2 | 8 | 97
Pedestrian Crash Behaviors:
Fatalities

## Slide 13
Top 10 Zip Codes for Pedestrian or Bicyclist Residence
One-third of total area-wide pedestrian and bicyclist crashes
No significant differences in environmental or behavioral characteristics compared to the rest of the metro area
Important for targeting most effective education and enforcement efforts

## Slide 14: Bicyclist Top 10 Zip Codes Number of Crashes by Zip Code Residence
32805 ………. 68
32839 ………. 59
32808 ………. 57
32792 ………. 57
32771/3 …….57
32807 ………. 56
32806 ………. 46
32822 ………. 44
34741 ………. 41
32825 ………. 36

## Slide 15: Pedestrian Top 10 Zip Codes Number of Crashes by Zip Code Residence
32808 ……..…. 80
32839 ………... 56
32822 ………... 55
32805 ……..…. 54
32818 ………... 44
32809 ………... 41
32811 ………... 39
34741 ……..…. 38
32771 ……..…. 34
32837 ………... 34

## Slide 16
Conclusions
Bicyclists
Increasing faster than pedestrians
Concentrated in low income neighborhoods and along multi-lane arterials
Most crashes involve sidewalk cycling and cycling against traffic
Most fatalities involve bicyclist failure to yield
Pedestrians
Concentrated in low income neighborhoods and along multi-lane arterials
42% of crashes are mid-block; 30% at intersections
Most fatalities involve pedestrian failure to yield

## Slide 17: Crashes and Infrastructure

## Slide 18: Lanes, Medians & Pedestrians
Number of Through Lanes | Change in Crashes per Mile | Change in Fatals per Mile | Number of Crashes |  | Number of Fatals | 
 |  |  | 2003/04 | 2012/13 | 2003/04 | 2012/13
2-Lane* | 1% | 44% | 100 | 101 | 9 | 13
4-Lane | 6% | 55% | 218 | 230 | 22 | 34
6-Lane | -4% | 19% | 139 | 133 | 26 | 31
8-Lane | -67% | -100% | 6 | 2 | 2 | 0
* On study network only
Mid-Block Crossing Crashes by Number of Lanes
Greatest increase in fatalities occurred on 4- and 6-lane roads.

## Slide 19: Lanes, Medians & Pedestrians
Number of Through Lanes | Change in Crashes per Mile | Change in Fatals per Mile | Number of Crashes |  | Number of Fatals | 
 |  |  | 2003/04 | 2012/13 | 2003/04 | 2012/13
2-Lane | 1% | 44% | 100 | 101 | 9 | 13
Divided (4+ Lanes) | -12% | 9% | 251 | 222 | 43 | 47
Undivided (4+ lanes) | 28% | 157% | 112 | 143 | 7 | 18
Mid-Block Crossing Crashes With and Without Medians
Greatest increase in fatalities occurred on multi-lane roads without medians.

## Slide 20
19%
0.5%
Overtaking Motorist
Percent of Crashes with Bicyclist in Each Position
Crashes Mitigated by Bike Lanes
29%

## Slide 21
Right Hook
Percent of Crashes with Bicyclist in Each Position
Crashes Aggravated by Bike Lanes
15%
23%
2%

## Slide 22
Left Cross
Percent of Crashes with Bicyclist in Each Position
Crashes Aggravated by Bike Lanes
7%
13%
5%

## Slide 23
10%
27%
Drive-out
Percent of Crashes with Bicyclist in Each Position
Crashes Aggravated by Bike Lanes
12%

## Slide 24
Wrong-Way Cyclist*
Percent of Crashes with Bicyclist in Each Position
Crashes Aggravated by Bike Lanes
21%
72%*
* Bicycling against traffic on a sidewalk or path is not illegal
17%

## Slide 25
Left Swoop
Percent of Crashes with Bicyclist in Each Position
Crashes Aggravated by Bike Lanes
13%
3%*
* Some crashes involving bicyclist failure to yield mid-block may have involved a bicyclist who was initially traveling with the flow on the sidewalk
2%

## Slide 26
Crashes Not Relevant to Bike Lanes
32%
15%
57%
Crash types not relevant to bike lanes should be a higher proportion if bike lanes are effective at reducing relevant types of crashes.

## Slide 27
Injury Severity
 |  | Number and Percent of Injuries and Fatalities |  |  | 
 |  | Travel Lane |  | Bike Lane/ Shoulder | 
Overtaking Crashes | Fatal & Incapacitating | 5 | 13% | 8 | 33%
 | Fatal & All Injuries | 20 | 50% | 19 | 79%
Crashes Aggravated by Bike Lanes | Fatal & Incapacitating | 8 | 15% | 10 | 12%
 | Fatal & All Injuries | 30 | 57% | 47 | 56%

## Slide 28
Similar Results
Copenhagen
(Jensen, 2007)
“The construction of cycle tracks has resulted in an 18-20% increase in cycle/moped traffic…”
“The construction of cycle lanes resulted in a 5-7% increase of cycle/moped traffic…”
Crash Change After Installation |  | 
 | Bike Lane | Cycle Track
Right Hook | +73% | +171%
Left Cross | NI | +34%
Drive-out | NI | NI
Overtaking | No change | -67%
Bicycle v. Pedestrian | NI | +128%
Bicyclist Left | No change | -51%
All Bicyclist Injuries | +49% | +30%

## Slide 29: Conclusions
Continue focus on improving pedestrian safety along multi-lane roads with better street lighting, medians and enhanced crossings
Education is necessary for bicyclists, pedestrians and motorists, regardless of what types of accommodations we provide
Installation of bikeways cannot be a one-size-fits-all approach