## Slide 1: SR 44 at Grand Avenue
Volusia County, FL
River to Sea CAC/TCC Meetings
May 17, 2016

## Slide 2: Agenda
Overview of Existing Conditions
Roundabout vs Signal Comparison
  Operations
  Safety
  Other Considerations
  Benefit-Cost
Overview of Current Concept
Next Steps

## Slide 3: Existing Intersection Configuration
BP Gas Station
SR 44
Grand Ave

## Slide 4: 2014 Annual Average Daily Traffic
2,300 AADT
1,000 AADT
9,800 AADT
4

## Slide 5: Existing Peak Hour Level-of-Service
AM
PM
C
C
C
E
5

## Slide 6: Crash Summary
Crash Statistics
  63% of crashes resulted in injury/fatality
  97% during dry conditions
  70% daytime / 30% nighttime
73% are angle crashes (22 of 30 crashes)
*Additional fatal crash in 2016
Year | 2010 | 2011 | 2012 | 2013 | 2014 | Jan-June 2015 | Total
Total Crashes | 1 | 3 | 5 | 9 | 3 | 9 | 30
Injury Crashes | 1 | 2 | 3 | 5 | 2 | 5 | 18
Fatal Crashes |  |  |  | 1 |  |  | 1*

## Slide 7: Operational Alternatives Comparison
Traffic Signal
LOS B in opening year
LOS C through 2035
NB & SB left-turn lanes needed
Roundabout
LOS A in opening year
LOS C through 2035
Single-lane allows up to 5% annual growth through 2035.
Intersection speed <25 mph

## Slide 8: Safety Alternatives Comparison
Traffic Signal
Expected Crash Reductions
  13% Total
  41% Injury
Reduce angle crashes
May increase rear-end
Higher speeds:
  more severe crashes
Roundabout
Expected Crash Reductions
  71% Total
  87% Injury
Fewer conflict points
Slower speeds:
  increase reaction time
  reduce severe crashes
FHWA Proven Safety Countermeasure

## Slide 9: Vehicle Conflict Points: REDUCED
Merging
Diverging
Crossing
Crossing conflicts eliminated at roundabout
NCHRP Report 672, Exhibit 5-2

## Slide 10: Severity of Conflicts: REDUCED
Severity is related to relative velocities of conflicting streams
Kansas Roundabout Guide, Second Edition

## Slide 11: Monetized Safety Benefits
Crash reductions converted to monetary benefit
  Crash costs tied to severity (PDO, Injury, Fatality)
Roundabout vs Existing Stop Control
  $8 million in crash reduction benefits
Roundabout vs Signal
  $4.4 million in additional crash reduction benefit for roundabout compared to signal

## Slide 12: Other Considerations
Design vehicles for both options include:
  Tractor-trailer trucks (WB-62FL with 53’ trailer)
  Buses
  Vehicles with boat trailers
  Emergency vehicles
Both options stay within existing right-of-way
Both maintain access to gas station

## Slide 13: Proposed Roundabout

## Slide 14: Over 25 Years of US Experience With Roundabouts
Source: Rodegerdts, L. A., “Status of Roundabouts in North America”, TRB 4th International Conference on Roundabouts, Seattle, WA, April 2014.

## Slide 15: Roundabouts in Rural Environments
Proven safety benefits at rural intersections
Proven truck accommodation
Proven compatibility with high speed roadways
  Additional considerations to transition speeds

## Slide 16: Aesthetic/Gateway Opportunities

## Slide 17: CR 561 at CR 455 (Lake County)

## Slide 18: CR 561 at CR 455 (Lake County)
Since Roundabout Opened (June 2015)
  No crashes
From 2002-2012
  32 Crashes
  2 Fatalities
  3.2 crashes per year
According to Lake County Public Information:

## Slide 19: Next Steps
Process
  Design-Build currently advertised
Cost
  $1,350,000 budgeted
Schedule
  250 Calendar Days
  June 17, 2016 Estimated Notice-To-Proceed

## Slide 20: Paola Kansas
1995-2000
  33 crashes
  42 injuries
2002 – Roundabout opened
  Annual average daily traffic 8,500
  20% truck traffic
2003-2008
  11 crashes (67 % reduction)
  ZERO injuries (100% reduction)
“Despite some initial trepidation, the roundabout has exceeded the expectations of the agency and the public for improving safety and accommodating freight movement.”