## Slide 1
River to Sea TPO Board
A Presentation to:
October 26, 2016

## Slide 2: Agenda
Study Status
Refined Alternatives Analysis
Potential Implementation Strategy
Next Steps
Discussion

## Slide 3: Study Process

## Slide 4: Refined Alternatives Analysis

## Slide 5: Bus Rapid Transit (BRT) Route Configuration
Potential Business Access and Transit (BAT) Lane
  6-lane and 8-lane sections
  Taylor Rd to Beresford Rd: roadway widening to create 6 lanes (median transitway option)
Mixed Traffic
  2-lane and 4-lane sections

## Slide 6: Rail Route Configuration
Separate right-of-way (ROW)
  SunRail Phase 2 North to S.R. 472
  I-95 to Williamson Blvd
Roadway median or side of road location
  S.R. 472 and U.S. 92
Roadway median location
  I-4
Side of road location
  Midway Ave

## Slide 7: Capital Cost Estimates in Millions
 |  | Alternative #4 BRT * | Alternative # 5 – Rail * |  | 
FTA SCC | Description |  | Baseline | S.R. 472 Alt | I-95 Undercrossing
10 | Guideway & Track Elements | $0.7 | $331.0 | $329.1 | $477.1
20 | Stations, Stops, Terminals, Intermodal | $6.5 | $25.1 | $25.1 | $25.1
30 | Support Facilities: Yards, Shops, Admin. Bldgs | $0.0 | $19.1 | $19.1 | $19.1
40 | Sitework & Special Conditions | $8.0 | 144.3 | $151.2 | $138.4
50 | Systems: Control Signals, Communications, Fare Collection | $2.0 | 159.4 | $159.4 | $159.4
60 | ROW, Land, Existing Improvements | $5.3 | $58.1 | $58.1 | $46.0
70 | Vehicles** | $32.0 | 51.0 | $51.0 | $51.0
80 | Professional Services | $6.1 | 217.2 | $218.9 | $262.1
90 | Unallocated Contingency | $0.4 | $67.9 | $68.4 | $81.9
Total |  | $61.1 | $1,073.1 | $1,080.3 | $1,260.2
* Cost estimates in 2015 dollars
** Vehicle cost include feeder bus service vehicle cost
FTA match (if eligible) 20% - 50%

## Slide 8: O&M Cost Estimates in Millions
Alternative | Service Frequency | Annual Service Hours | No. of Vehicles /Train Sets Required | Annual O&M Cost** | Feeder Bus Cost* | Total O&M Cost**
Alternative #4 -to DeBary Station | 30 min, 14 hrs/day, 7 days/week | 53,000 | 18 | $4.3 | $11.5 | 
Alternative #4 - to DeLand Station | 30 min, weekday peak | 7,600 | 5 | $0.6 |  | 
Total BRT |  | 60,600 | 23 | $4.9 | $11.5 | $16.4
Alternative #5 - Main Line | Same as SunRail | 10,600 | 5 | $16.8 | $8.5 | 
Alternative #5 - Shuttle to DeLand | Same as SunRail | 5,400 |  | $8.6 |  | 
Rail Total |  | 16,000 | 5 | $25.4 | $8.5 | $34.0
* Feeder bus costs do not include costs for proposed TDP service improvements
** Cost estimates in 2015 dollars

## Slide 9: Ridership Projections
725
Source: FTA STOPS model
475
428,500
2050
618,500
119,700
179,000

## Slide 10: New and Small Starts Project Evaluation and Rating
Overall
Rating
Summary
Ratings
Individual Criteria Ratings
Mobility Improvements
(16.66%)
Project Justification*
(50% of Overall Rating)
Overall Project Rating
Local Financial
Commitment*
(50% of Overall Rating)
Environmental Benefits
(16.66%)
Congestion Relief
(16.66%)
Cost-Effectiveness
(16.66%)
Economic Development
(16.66%)
Land Use
(16.66%)
Current Condition
(25%)
Commitment of Funds
(25%)
Reliability/Capacity
(50%)
*Must be al least “Medium” for project to get “Medium” or better Overall Rating
*Must be al least “Medium” for project to get “Medium” or better Overall Rating

## Slide 11: FTA Project Justification Rating Assessment
Both build alternatives in general scored poorly against criteria
BRT more cost-effective than rail
Lack of development density and transit-oriented development results in poor land use score
Local financial commitment currently not in place to result in a medium to high rating
Conclusion: Neither alternative would achieve high enough rating to be competitive for federal funding.
Criterion | Alternative #4 - BRT | Alternative #5 - Commuter Rail
Mobility Improvements | Low | Low
Cost-Effectiveness | Medium | Low
Congestion Relief | Medium-Low | Medium
Environmental Benefits | Low | Medium-Low
Land Use | Low | Low
Economic Development | Low | Low

## Slide 12: Where do We Go from Here?
    Provide officials with road map on where we need to go to implement an enhanced transit system
    Need to identify strategies and tools that we can start to put in place now
Conclusion: Develop an Implementation Strategy

## Slide 13: Potential Implementation Strategy

## Slide 14: Two-Component Strategy
Progressive transit service and facility improvements
Strategies and policies to foster transit-oriented development

## Slide 15: Transit Improvement Strategy
ID strategy for added local transit O&M revenues
Implement bus service improvements related to new revenue sources
Integrate transit priority and stop improvements into roadway improvements
Develop new transit centers and initial park-n-rides
Potential BRT service in the US 92 and/or US 17/92 corridors, with added feeder bus connections improvements
Evaluate preservation of ROW for future premium transit corridor(s)
Potential rail extension toward Daytona Beach
1
2
3
4
5
6
7

## Slide 16: Land Development Strategies
Growth management and land conservation policies focusing on development density and market trends supportive of transit
Develop conceptual plans for designated BRT and rail transit station areas
Implement zoning changes that support major transit investment in transit station areas
Implement strategies to promote transit-supportive planning and station area development
Develop affordable housing plans along transit corridors
5
4
3
2
1

## Slide 17
Transit and Density Relationship
Population and employment densities affect the viability of transit mode
Higher population densities and/or employment centers help justify premium rail options
Higher densities help justify greater transit service levels

## Slide 18
Effects of population and employment
Highest-order mode to support future development density (year 2040)
Primarily support local bus options
Potential BRT/LRT options along ISB
Mode Applicability Based on Densities in Study Area

## Slide 19: Densities: Study Area vs. SunRail Stations
Area | 2010 Density (per sq.mi.) |  | 2040 Density (per sq.mi.) | 
 | Population | Employment | Population | Employment
Study Area | 200 | 270 | 640 | 740
Seminole County | 1,090 | 1,540 | 1,650 | 2,430
Downtown Orlando | 3,600 | 33,040 | 11,540 | 39,410
Orange County | 1,550 | 3,500 | 3,520 | 5,100

## Slide 20: Transit Oriented Development (TOD) Assessment
Analysis of TOD potential conducted at ten potential premium transit stations
Particular focus at I-4/SR 472
Process
  Stakeholder interviews
  Application of FDOT TOD Readiness Tool
  Strategy and policy recommendations

## Slide 21: Next Steps

## Slide 22: Remaining Schedule
Final Elected Official Briefings – September- October 2016
Issue Project Summary Report – December 2016

## Slide 23: Discussion

## Slide 24
General Discussion/Questions